## Slide 1
Memory: Introduction

## Slide 2
2
Picture of Memory
You can think of memory as being one big array of data.
  The address serves as an array index.
  Each address refers to one word of data.
You can read or modify the data at any given memory address, just like you can read or modify the contents of an array at any given index.
Word
16-bit/32-bit

## Slide 3
3
Memory Signal Types
Memory signals fall into three groups
  Address bus - selects one of memory locations
  Data bus
    Read: the selected location’s stored data is put on the data bus
    Write (RAM): The data on the data bus is stored into selected locations
  Control Signals - specifies what the memory is to do
    Control signals are usually active low
    Most common signals are:
      CS: Chip Select; must be active to do anything
      OE: Output Enable; active to read data
      WR: Write; active to write data

## Slide 4
Random Access Memory

## Slide 5
5
Random Access Memories
So called because it takes the same amount of time to address any particular part
Types of RAM
  Static RAM (SRAM), fast, expensive
  Dynamic RAM (DRAM), slow, cheap
How is memory accessed?
  Address Lines, Data Lines
  Control Signals (R/W, chip select, …)

## Slide 6
6
Simple View of RAM
Of some word size n=4,8,16 ….
Some capacity 2k
k bits of address line, k=10,11,..
  Has a read line
  Has a write line

## Slide 7
7
1K x 16 memory
Variety of sizes
  From 1-bit wide
Issue is no. of pins
Memory size specified in bytes
  1K x 16 bit  2KB memory
10 address lines and 16 data lines

## Slide 8
8
Chip Select and R/W Lines
R/W Lines enable reading/writing
Usually a chip select line is used.
Why?
  To enable RAM chip to be accessed.

## Slide 9
9
Memory: Writing
Sequence of steps
  Setup address lines
  Setup data lines
  Activate write line (maybe a pos edge)
The write cycle time is the maximum time from the application of the address to the completion of all internal memory operations required to store a word.

## Slide 10
10
Writing: Timing Waveforms
CPU operates at 50 MHz (20 ns)
4 clock cycles to perform a write

## Slide 11
11
Memory Reading
Steps
  Setup address lines
  Activate read line
  Data available after specified amount of time
Read cycle usually is shorter than write cycle.

## Slide 12
12
Memory Waveform: Reading
CPU operates at 50 MHz (20 ns)
65 ns required for a read cycle

## Slide 13
Static RAM

## Slide 14
14
MOSFET: Metal Oxide
Semiconductor
Field Effect Transistor
A voltage controlled device
Dissipates less power
Achieves higher density on an IC
Has full swing voltage 0 > 5V

## Slide 15
15
Static RAM: 4T and 6T
Six Transistors to implement a memory cell

## Slide 16
16
Pin Diagram

## Slide 17
SRAM Cell
17
VDD
GND
VDD
VDD
VDD

## Slide 18
Dynamic RAM

## Slide 19
19
Dynamic Memory
Dynamic memory is built with capacitors.
  A stored charge on the capacitor represents a logical 1.
  No charge represents a logic 0.
However, capacitors lose their charge after a few milliseconds. The memory requires constant refreshing to recharge the capacitors. (That’s what’s “dynamic” about it.)
Dynamic RAMs tend to be physically smaller than static RAMs.
  A single bit of data can be stored with just one capacitor and one transistor, while static RAM cells typically require 4-6 transistors.
  This means dynamic RAM is cheaper and denser—more bits can be stored in the same physical area.

## Slide 20
20
Dynamic RAM
Capacitor can hold charge
Transistor acts as gate
  No charge is a 0
  Can close switch & add charge to store a 1
Then open switch (disconnect)

## Slide 21
21
DRAM Cell

## Slide 22
DRAM read Operations
  Precharge bit line to VDD/2.
  Take the word line HIGH.
  Detect whether current flows into or out of the cell.
  Note: cell contents are destroyed by the read!
  Must write the bit value back after reading.
22

## Slide 23
DRAM write Operations
  Take the word line HIGH.
  Set the bit line LOW or HIGH to store 0 or 1.
  Take the word line LOW.
  Note: The stored charge for a 1 will eventually leak off.
23

## Slide 24
24
Dynamic RAM (… continued)
(a)
(c)
(f)
(g)
Select
B
T
C
DRAM cell
To Pump
(b)
(d)
(e)
Stored 1
Stored 0
Write 1
Write 0
Read 1
Read 0
Notes: School of Engineering
24
Warning: (d), (e), (f), and (g) are animated. Each animation is triggered with a mouse click
and goes through two steps at 1 second intervals.

## Slide 25
25
DRAM Characteristics (Why Slow!)
Destructive Read
  When cell read, charge removed
  Charge must be restored after a read
Refresh
  Capacitors are not perfect! there’s steady leakage
  Charge must be restored periodically
DRAM are dense (lots of cells) so there are many address lines.
  To reduce the physical size of DRAM we can reduce the number of pins by applying the address lines serially in two parts:
    Row Address, and then
    Column Address

## Slide 26
26
How DRAM Works
A7A6A5A4
A3A2A1A0
A7A6A5A4A3A2A1A0