## Slide 1: Random Access Protocols
Slotted Aloha
Pure(Unslotted) Aloha
Carrier Sense Multiple Access(CSMA)
CSMA with Collision Detection(CD)
Cahit Barkın Özer 2018556059

## Slide 2: Random access protocols
when node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes ➜ “collision”,
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 3: Slotted ALOHA
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with prob. p until success

## Slide 4: Slotted ALOHA
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E
C=collision slot
E=empty slot
S=successful slot

## Slide 5: Slotted ALOHA: efficiency
suppose: N nodes with many frames to send, each transmits in slot with probability p
probability that given node has success in a slot = p(1-p)N-1
probability that any node has a success = Np(1-p)N-1
max efficiency: find p* that maximizes Np(1-p)N-1
for many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives:
max efficiency = 1/e = 0.37
efficiency: long-run fraction of successful slots (many nodes, all with many frames to send)
at best: channel
used for useful
transmissions 37%
of time!
!

## Slide 6: Pure (unslotted) ALOHA
unslotted Aloha: simpler, no synchronization
when frame first arrives
  transmit immediately
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]

## Slide 7: Pure ALOHA efficiency
P(success by given node) = P(node transmits) .
P(no other node transmits in [t0-1,t0] .
P(no other node transmits in [t0-1,t0]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting n
= 1/(2e) = .18
even worse than slotted Aloha!

## Slide 8: CSMA (carrier sense multiple access)
CSMA: listen before transmit:
if channel sensed idle: transmit entire frame
if channel sensed busy, defer transmission
human analogy: don’t interrupt others!

## Slide 9: CSMA collisions
collisions can still occur: propagation delay means two nodes may not hear each other’s transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in in determining collision probability
spatial layout of nodes

## Slide 10: CSMA/CD (collision detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: received signal strength overwhelmed by local transmission strength
spatial layout of nodes

## Slide 11: Ethernet CSMA/CD algorithm
1. NIC receives datagram from network layer, creates frame
2. If NIC senses channel idle, starts frame transmission. If NIC senses channel busy, waits until channel idle, then transmits.
3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame !
4. If NIC detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  longer backoff interval with more collisions

## Slide 12: CSMA/CD efficiency
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!

## Slide 13: Thank you for listening
References:
Computer Networking: A Top Down Approach 6th edition book