## Slide 1: Voice Over LTE
Cahİt Barkın Özer 2018556059
Rüveyda Kılıç 2017556036
Berk Eroğlu 2018556027

## Slide 2: Content
1. Introduction
a. What is VoLTE ?
b. History of VoLTE
2. Analysis
a. Advantages of VoLTE
b. Disadvantages of VoLTE
3. Comparison with VoIP
a. Similarities between VoLTE and VoIP
b. Differences between VoLTE and VoIP
References

## Slide 3: What is VoLTE?
Voice over Long-term evolution (VoLTE) is an internet-based communication data transfer technology for phones, internet of things and wearable devices.
VoLTE is based on IP Multimedia Subsystem(IMS) . This method results in a voice service being provided as traffic flows inside the LTE data carrier, without dependency the circuit-switched voice network to be in the call route.
VoLTE has a speech and network range up to three times that of older 3G UMTS and up to six times that of 2G GSM and packet headers are smaller than VoIP / LTE headers so they use less bandwidth.

## Slide 4: History of VoLTE
In 2009, 12 major telecommunication companies partnered and suggested a solution for the VoLTE network. The solution was IMS based and project was called One Voice. One Voice was the idea of using existing standards to produce a generic solution with the VoIP network. GSMA (Global System for Mobile Communication) started to work on the idea to make the solution official for general use in February 2010. When GSMA's VoLTE solution was released, it was funded by 40 organizations worldwide.
In 2012, worlds first commercial VoLTE service launched with worlds first VoLTE phone LG Connect 4G by MetroPCS in Texas USA. By 2020 all brand new mobile phones support VoLTE technology.

## Slide 5: Advantages of VoLTE
Delivers clear and high definition voice: The major benefit of VoLTE is that the efficiency of the call is better than 3G or 2G when much more data can be transmitted over 4G . The compression method used in general calls uses an 8 kbps codec, but with VoLTE the codec can use 13kbps codec. The frequency range also increased from 300-3400 Hz range to 50-7000 Hz range. This means higher quality of a call than a regular mobile call. The calls are delivered over the LTE networks so the latency (Delay) is much lower when compared to current networks.
Faster connections: VoLTE provides connection twice time quicker than the previous methods. Some frequencies of 4G networks have much wider reach than 2G or 3G networks so it provides better indoor coverage.

## Slide 6: Advantages continued
Provides a more efficient use of your network sources: It would enable a simpler network that is more cost-effective to maintain by allowing service providers to eventually handle only one network instead of providing voice services through an older 2G, 3G voice network. Rich Conversations: Besides calling, operators can offer a range of services known as RCS (Rich Communication Services). These services include features such as video calls, data transfer and simultaneous translation during the call.

## Slide 7: Disadvantages of VoLTE
We emphasize that VoLTE is a new technology and as such it still needs to be improved for quality service. So far, we can list the disadvantages as follows.
Limited to certain devices: Only 4G terminals will support VoLTE. For example, Xiaomi Mi4 named cellphone does not support 4G VoLTE option in India.
Disconnection of the call: This is a new technology and 4G network uses antennas different from other technologies hence VoLTE still cannot guarantee a call without disconnections.

## Slide 8: Disadvantages continued
Cannot communicate between operators: In principle it is only possible to call with VoLTE between the customers of the same operator. For example calls between one operator and another cannot be made with VoLTE.
Price change: Now that we are used to the flat rate for calls. VoLTE calls use the data network. That is why the expense of VoLTE calls is reflected in our bill. But nowadays VoLTE calls are usually cost at similar rate as traditional calls.
Battery life: There is no general opinion, although some research showed that the VoLTE feature reduces the battery life of the device by half. One research says that VoLTE uses continuous stream of small packets with low data rate, so it maximizes the battery life.

## Slide 9: Comparison of VoLTE Against VoIP
What is VoIP (Voice Over IP)?
Voice over Internet Protocol (VoIP) is a technology used to transmit communication data over Internet Protocol (IP) networks.
Similarities Between VoLTE and VoIP
They both use Internet to transmit voice data.
They both use “Packet Switching” technology means that they are transferring your voice data as binary 1’s and 0’s, rather than analogue method.
They both use same technology, only difference is VoLTE transfers voice data to clients over 4G cell towers.

## Slide 10: Differences of VoLTE and VoIP
VoIP is an older technology than VoLTE. But that does not mean VoLTE is better than VoIP.
VoLTE uses 4G technology. VoIP uses 2G, 3G, Ethernet and Wi-Fi.
VoLTE provides more scalability: VoIP is supported by the Web and by VoIP phones, but VoLTE is supported by all modern smartphones and devices.

## Slide 11: Differences continued
VoLTE is more costly to implement. VoIP can use old copper cables known as ADSL to transmit voice data, but VoLTE needs 4G supported cell towers. That comes with costs for service provider and client.
VoIP may provide less latency. Usually, VoIP transmit voice data over network cables, but VoLTE always must transmit voice data from cell towers. 4G is a wireless radio technology and radio waves can be affected by distance, weather, other radio waves and buildings . Those issues may increase latency of VoLTE, but VoIP usually uses cables that cannot affected by weather and radio waves.

## Slide 12: References
1.Introduction
[1] Wikipedia contributors.(2020,November,25).Voice over LTE : [https://en.wikipedia.org/wiki/Voice_over_LTE]
[2] No name.(no date) What is Voice over LTE, VoLTE :
[https://www.electronics-notes.com/articles/connectivity/4g-lte-long-term-evolution/volte-voice-over-lte.php]
[3] Prashant Panigrahi. (?2016).VoLTE History and Timeline : [http://www.3glteinfo.com/volte-history-timeline/]
2. Analysis
[4] Ankit Bhardwaj(2018, July,1) What is VoLTE technology Advantages and Disadvantages:
[https://teknologya.com/what-is-volte-technology-advantages-and-disadvantages/]
[5] Gizbot Bureu(2017, March,23) VoLTE benefits and disadvantages:
[https://www.gizbot.com/mobile/features/volte-benefits-and disadvantages/articlecontent-pf71893-039343.html]
[6] No name (2019, April,11) What is VoLTE: [https://www.summanetworks.com/blog/what-is-volte]

## Slide 13: References
3. Comparison with VoIP
[7] Wikipedia contributors. (2020,December,1). Voice over IP: [https://en.wikipedia.org/wiki/Voice_over_IP]
[8] Wikipedia contributors. (2020, November,29). Packet switching: [https://en.wikipedia.org/wiki/Packet_switching]
[9] Katherine Stone. (2020, August,29). The history of VoIP and internet telephony:
[https://getvoip.com/blog/2014/01/27/history-of-voip-and-internet-telephones/]
[10] Pulsar360. (2018. July, 10). What is the difference between VoIP and VoLTE:
[https://www.pulsar360.com/blog.aspx?p=what-is-the-difference-between-voip-and-volte-180710]
[11] Wikipedia contributors. (2020, November , 20). 4G: [https://en.wikipedia.org/wiki/4G]
[12] No name. (No date). Causes of Wifi interference:
[https://activereach.net/support/knowledge-base/connectivity-networking/wifi-interference/]